## Slide 1: Integrated circuit logic families
Presented by Jamil Rayhan
ID: 18CSE061

## Slide 2: Introduction
Logic gates are available in the form of Integrated circuit( IC’s)
As per the level of integration, the IC’s can accommodate more number of logic gates and digital functions.
These forms are referred as logic family

## Slide 3: Logic family
Logic Families indicate the type of logic circuit used in the IC.
A Circuit configuration or arrangement of the circuit elements in a special manner will result in a particular Logic Family.
The set of digital ICs belonging to the same logic family are electrically compatible with each other

## Slide 4: Characteristics of logic families
The main characteristics of Logic families include:
    Speed
    Fan-in
    Fan-out
    Noise Immunity
    Power Dissipation

## Slide 5
Speed: Speed of a logic circuit is determined by the time between the application of input and change in the output of the circuit.
Fan-in: It determines the number of inputs the logic gate can handle.
Fan-out: Determines the number of circuits that a gate can drive.
Noise Immunity: Maximum noise that a circuit can withstand without affecting the output.
Power: When a circuit switches from one state to the other, power dissipates.
Characteristics of logic families(cont.)

## Slide 6: Basic classification of logic families

## Slide 7: Unipolar Logic Families
Its stands for Metal Oxide Semiconductor.
In these MOSFETs (Metal oxide semiconductor field-effect transistor) are fabricated on chip.
It is used in LSI [Large scale integration] field because more MOSFETs can be packed into the same chip area.

## Slide 8: Types of Unipolar Family
PMOS Family
NMOS Family
CMOS Family

## Slide 9: CMOS
CMOS stands for “Complementary Metal Oxide Semiconductor”.
One of the most popular technology in computer chip design industry
Broadly used to form integrated circuits.
CMOS devices are chips in which both P-channel and N-channel enhancement MOSFETs are connected in a push-pull arrangement.

## Slide 10: CMOS
Complementary Metal Oxide Semiconductor Transistor consist of PMOS and NMOS.

## Slide 11
CMOS Inverter
Input | Logic Input | Output | Logic Output
0v | 0 | Vdd | 1
Vdd | 1 | 0v | 0

## Slide 12: Applications
Technology like CMOS is used in different chips like,
      Microcontrollers
      Microprocessors
      Static RAM(SRAM)
      Data converters
      Image sensors

## Slide 13: Advantages of CMOS
The main advantage of CMOS is the much smaller power dissipation.
CMOS are simple , small in size ,cheaper in fabrication.
Reduce the complexity of the circuit.
High noise immunity.

## Slide 14: Disadvantages of cmos
Not Bipolar
Some circuit are not practicable.
Difficult to implement.

## Slide 15: Bipolar Families
Bipolar transistors are fabricated on a chip in digital integrated circuits.
Bipolar technology is preferred for SSI [ Small scale integration ] and MSI [ Medium scale integration ] because it is faster.

## Slide 16: Types of Bipolar Families
Non Saturated
    Schottky TTL
    Emitter Coupled Logic(ECL)
Saturated
    Resistor Transistor Logic (RTL)
    Diode Transistor Logic (DTL)
    Transistor- Transistor Logic (TTL)

## Slide 17: What is TTL?
It’s a logic family built from Bipolar Junction Transistors.
Its name signifies that transistors perform both the logic function and the amplifying function.
Widely used logic family

## Slide 18: Transistor-Transistor logic
Two-input TTL NAND gate with a simple output stage

## Slide 19: Advantages of TTL
TTL provides very high speed .
TTL is more reliable .
TTL needs lower power for any operation .
TTL can stack the transistors to make for fast pull up and pull down .
TTL circuits are not so complicated .

## Slide 20: Disadvantages of TTL
Consumes more power compares to CMOS family and hence it is not suitable for battery powered devices over ECL and CMOS .
It has fan out of 10 which is less compare to CMOS .
Logic circuit having N fan out can drive N logic inputs.

## Slide 21: Thank you